## Slide 1: Circuit Card Inquiry Lab
Jonathan Adams
RBT125

## Slide 2: Card 7: Noninverting Amplifier
This is a basic circuit that are from amplifiers. This circuit helps achieve the non-inverted output at the final stage. “The circuit designed for a non-inverting amplifier consists of a basic op-amp where the input is connected to a non-inverting terminal. The output obtained from this circuit is a non-inverted one. This is again feedback towards input but to the inverting terminal via a resistor. Further, one more resistor is connected to the inverting terminal in concern to connect it to the ground. Hence the overall gain of the circuit is dependent on these two resistors that are responsible for the feedback connection. Those two resistors will behave as a voltage divider of the feedback fed to the inverting terminal. Generally R2 is chosen to be greater than the R1.” (WatElectronics, 2022)

## Slide 3: Where is the circuit used?
This circuit is used in many different electronics that use amplifiers and electrical engineering applications. “The voltage follower or unity gain buffer is a special and very useful type of Non-inverting amplifier circuit that is commonly used in electronics to isolated circuits from each other especially in High-order state variable or Sallen-Key type active filters to separate one filter stage from the other. Typical digital buffer IC’s available are the 74LS125 Quad 3-state buffer or the more common 74LS244 Octal buffer.” (Storr, 2022)

## Slide 4: Advantages
The output signal is obtained without phase inversion.
In comparison to the impedance value of the input at the inverting amplifier is high in the non-inverting amplifier.
The voltage gain in this amplifier is variable.
Better matching of impedance can be obtained with the non-inverting amplifiers.
It has a positive voltage gain.
(WatElectronics, 2022)

## Slide 5: Disadvantages
More stages are utilized based on the requirement of achieving desired gain.
Based on the respective amplifiers chosen the input and the output resistance gets varied.
(WatElectronics, 2022)
There are also other disadvantages such as the risk of amplifying noise and the possibility of stray capacitance.

## Slide 6: Variations of the circuit
Besides the inverting form, summing amplifiers may also be produced in a noninverting form. Noninverting summers generally exhibit superior high frequency performance when compared to the inverting type. The differential amplifier configuration is a combination of the inverting and noninverting voltage amplifiers. .” (Libretexts, 2022)
An op-amp has two differential input pins and an output pin along with power pins. Those two differential input pins are inverting pin or Negative and Non-inverting pin or Positive. An op-amp amplifies the difference in voltage between this two input pins and provides the amplified output across its Vout or output pin. (Non-inverting Operational Amplifier, n.d.)

## Slide 7: References
Libretexts. (2022). 4.2: Inverting and noninverting amplifiers. Engineering LibreTexts. https://eng.libretexts.org/Bookshelves/Electrical_Engineering/Electronics/Operational_Amplifiers_and_Linear_Integrated_Circuits_- _Theory_and_Application_(Fiore)/04%3A_Basic_Op_Amp_Circuits/4.02%3A_Inverting_and_Noninverting_Amplifiers
Non-inverting operational amplifier. (n.d.). https://circuitdigest.com/tutorial/non-inverting-operational-amplifier
Storr, W. (2022). Non-inverting operational amplifier. Basic Electronics Tutorials. https://www.electronics-tutorials.ws/opamp/opamp_3.html
WatElectronics. (2022, October 31). Non-Inverting Amplifier Theory,GaiN, Output Waveforms & Applications. WatElectronics.com. https://www.watelectronics.com/non-inverting-amplifier-theory-circuit-diagram-gain-output-wave-forms-applications/